## Slide 1: SIP and NAT
Dr. Jonathan Rosenberg
Cisco Fellow

## Slide 2: What is NAT?
Network Address Translation (NAT)
  Creates address binding between internal private and external public address
  Modifies IP Addresses/Ports in Packets
  Benefits
    Avoids network renumbering on change of provider
    Allows multiplexing of multiple private addresses into a single public address ($$ savings)
    Maintains privacy of internal addresses
Client
N
A
T
N
A
T
S: 1.2.3.4:8877
D: 67.22.3.1:80
Binding Table
Internal External
10.0.1.1:6554 -> 1.2.3.4:8877
S: 10.0.1.1:6554
D: 67.22.3.1:80
IP Pkt
IP Pkt

## Slide 3: Problem: Getting SIP Through NATs
N
A
T
INVITE sip:12345@b.com
m=audio 3456 RTP/AVP 0
c=IN IP4 10.0.1.1
RTP to 10.0.1.1

## Slide 4: Solution Space
Application Layer Gateways (ALGs)
Session Border Controllers (SBC)
Simple Traversal of UDP Through NAT (STUN)
Traversal Using Relay NAT (TURN)
Interactive Connectivity Establishment (ICE)

## Slide 5: Application Layer Gateway
N
A
T
INVITE sip:12345@b.com
m=audio 3456 RTP/AVP 0
c=IN IP4 10.0.1.1
RTP to 10.0.1.1
INVITE sip:12345@b.com
m=audio 1234 RTP/AVP 0
c=IN IP4 19.1.3.2
ALG
NAT also modifies SIP
messages to fix them up!

## Slide 6: ALG Benefits and Drawbacks
Drawbacks
  Doesn’t work when security turned on
  Hard to diagnose problems
  Requires network upgrade to support new app
  Frequent implementation problems (lack of expertise)
  Incentives mismatched
Benefits
  No change to clients or servers

## Slide 7: Session Border Controller
N
A
T
INVITE sip:12345@b.com
m=audio 3456 RTP/AVP 0
c=IN IP4 10.0.1.1
SBC
9.8.7.6
INVITE sip:12345@b.com
m=audio 3225 RTP/AVP 0
c=IN IP4 9.8.7.6
RTP to
9.8.7.6
SBC relays
RTP back to
source

## Slide 8: SBC Benefits and Drawbacks
Drawbacks
  Expensive media relaying
  Interferes with some SIP extensions
  Breaks more advanced SIP security
Benefits
  No change to clients or NATs
  Works with basic SIP security mechanisms
  Easier to diagnose

## Slide 9: Simple Traversal of UDP Through NAT (STUN)
N
A
T
What is my IP address
and port please?
STUN
Server
9.8.7.6
INVITE sip:12345@b.com
m=audio 3472 RTP/AVP 0
c=IN IP4 1.2.3.4
RTP to
1.2.3.4
1.2.3.4
Its
1.2.3.4: 3472

## Slide 10: STUN Benefits and Drawbacks
Drawbacks
  Doesn’t always work
Benefits
  No change to servers or NATs
  Works with all SIP security mechanisms
  Can support non-VoIP apps (e.g., games)

## Slide 11: Traversal Using Relay NAT (TURN)
N
A
T
Give me an IP address
and port please?
TURN
Server
9.8.7.6
INVITE sip:12345@b.com
m=audio 2376 RTP/AVP 0
c=IN IP4 9.8.7.6
RTP to
1.2.3.4
1.2.3.4
9.8.7.6:
2376

## Slide 12: TURN Benefits and Drawbacks
Drawbacks
  Expensive Media Relaying
Benefits
  No change to servers or NATs
  Works with all SIP security mechanisms
  Can support non-VoIP apps (e.g., games)

## Slide 13: Interactive Connectivity Establishment (ICE)
Hybrid of STUN and TURN
P2P NAT Traversal
Widely Deployed on Internet
Popular with Application Providers

## Slide 14: ICE Step 1: Allocation
Before Making a Call, the Client Gathers Candidates
Each candidate is a potential address for receiving media
Three different types of candidates
  Host Candidates
  Server Reflexive Candidates (STUN)
  Relayed Candidates (TURN)
TURN
Host
Candidates reside on the agent itself
STUN candidates
are addresses residing on a NAT
NAT
NAT
TURN candidates reside on a TURN server
STUN

## Slide 15: ICE Step 2: Create Offer
Each candidate is placed into an a=candidate attribute of the offer
Each candidate line has IP address and port plus other info needed for ICE
c=IN IP4 192.0.2.3
t=0 0
m=audio 45664 RTP/AVP 0
a=rtpmap:0 PCMU/8000
a=candidate:1 1 UDP 2130706178 10.0.1.1 8998 typ host
a=candidate:2 1 UDP 1694498562 192.0.2.3 45664 typ srflx raddr 10.0.1.1 rport 8998

## Slide 16: ICE Step 3: Send INVITE
Caller sends a SIP INVITE as normal
No ICE processing by SIP servers
SIP
Server
INVITE

## Slide 17: ICE Step 4: Allocation
Called party does exactly same processing as caller and obtains its candidates
Recommended to not yet ring the phone!
TURN
NAT
NAT
STUN

## Slide 18: ICE Step 5: Provisional Response
Callee sends a provisional response containing its SDP with candidates
As with INVITE, no processing by proxies
Phone has still not rung yet
SIP
Proxy
1xx

## Slide 19: ICE Step 6: Verification
Each agent pairs up its candidates (local) with its peers (remote) to form candidate pairs
Each agent sends a STUN-based ping on each pair, starting at highest priority
If a response is received the check has succeeded and we know media can flow on that pair!
TURN
Server
NAT
NAT
TURN
Server
NAT
NAT
1
2
3
4
5

## Slide 20: ICE Benefits and Drawbacks
Drawbacks
  Requires client changes
  Requires other side to support it
Benefits
  Always Works
  No change to servers or NATs
  Works with all SIP security mechanisms
  Minimum Media Relaying
  Can support non-VoIP apps (e.g., games)
  Built-In Anti-DOS
  Eliminates Ghost Rings