## Slide 1: Quality of Service for Internet Telephony
Jonathan Rosenberg

## Slide 2: Talk Overview
What is QoS
Intserv
  Model
  RSVP
  Guaranteed Load
  Controlled Load
Differentiated Services
Diffserv and VoIP
  Packet classification problem
Intserv and VoIP
  coupling problem

## Slide 3: Quality of Service = QoS
Best Effort Service Model
  No guarantees on order
  No guarantees on delay
  No guarantees on jitter
  No guarantees on loss
  Network does the best it can
  All traffic treated equally
Drawbacks for IP Telephony
  Loss rates above 5%
  Delays above 200ms
  Jitter above 100ms
What is Quality of Service?
  Statement about the performance of the network in its delivery of packets
  Quantitative or Qualitative
  Quantitative metrics
    Loss: usually mean, but correlation or CLP important
    Delay: one way vs. RTT
    Jitter: variance in delay or avg. difference in send and receive times
    Bandwidth: b/s or B/s

## Slide 4: Some Terminology
5-tuple
  Combination of Source/Dest IP, Source/Dest Port and Protocol
Packet Filters
  Rules that identify packets, usually based on 5-tuple
Flow
  A group of packets with the same 5-tuple
Packet Classification
  Act of filtering packets
Scheduling Algorithm
  When multiple packets contend for a link, the mechanism by which packets are chosen to be sent
Buffer Management
  Rules by which memory resources of a router are allocated to different packets
Weighted Fair Queueing
  A scheduling algorithm that can allocate specific bandwidths to different flows
  Excess bandwidth re-distributed proportionally

## Slide 5: More Terminology
Policer
  A component of a router which checks whether a flow has certain properties
Shaper
  A component of a router which delays or drops packets so that they leave the router with a specific property
Leaky Bucket
  An algorithm for policing or shaping based on average rate and burstiness
Random Early Drop (RED)
  A buffer management algorithm that randomly drops packets before congestion
  Good properties for TCP
Generalized Processor Sharing (GPS)
  A theoretical scheduling algorithm that models packet flows as a fluid
  WFQ is an approximation to GPS
Drop from Front
  A buffer management algorithm that drops excess packets from front of queue

## Slide 6: Integrated Services Model
New service model for Internet
Two components
  Type of service provided by network
  How service is requested
Separation of components
  New services defined and supported by same request protocols
  Many ways (SNMP) to configure single service
Intserv Model similar to ATM
  Service requested end to end
  Resources reserved along all routers
  Admission control at all routers
  Policing needed at routers
  Shaping may be needed at routers
Two types of service
  Controlled Load
  Guaranteed
Reservation through RSVP

## Slide 7: ReSource ReserVation Protocol (RSVP)
Receivers make reservations
  Senders send PATH messages
  Receivers send RESV messages to reserve
PATH Messages
  Follow data path for flow being reserved
  Create path State, point to previous hop router
  Define flow
RESV Messages
  Follow reverse of PATH
Sender
Receiver

## Slide 8: Why Receiver Oriented?
Multicast!!!
  Senders don’t know receivers
  Receivers might be heterogeneous
  Receivers receive the benefit of reservations
RSVP in multicast
  Not all receivers need make a reservation
  Receivers can make different reservations
  Reservations merged at branch points

## Slide 9: RSVP Features
Routing Protocol Independence
  Path followed by messages determined by BGP, RIP, OSPF
  Path may change mid-reservation
  Path not selected based on ability to meet QoS requirements
Soft State
  Reservations refreshed periodically
  If not refreshed, they time out
  Handles route changes well
  Handles changes in reservations
Simplex
  Reservation from A to B does not imply reservation from B to A
  Duplex reservations require two simplex reservations
Idempotence
  Each reservation processed independently of past reservations
  Deals with soft-state nature of RSVP
  Makes changing reservations trivial
  Processing penalty

## Slide 10: Message Details
PATH messages
  Sender Template
    identifies sender
    Source IP and port
  Tspec: Transmission Specification
    Description of source data
    Usually leaky bucket
RESV Messages
  Filterspec
    Identifies sender
  Tspec
  Rspec
    Desired QoS for reservation
PATH
Sender Template
TSpec
RESV
Filterspec
Flowspec
RSpec
TSpec

## Slide 11: Leaky Bucket
A way to characterize a data source
Three parameters
  Average rate r
  Peak rate p
  Bucket depth b
A flow is conformant if
  Rate never exceeds p
  Average rate r
  Never more than b consecutive packets at rate p
Tokens enter at rate r
Depth b
p
Avg. rate
Checks rate not more than p

## Slide 12: Reservation Styles
For multicast, what sender is reservation for?
  Can be many senders
  Reservation can be for a specific set (explicit) or any (wildcard)
If reservation is for many senders, how is bandwidth allocated?
  Shared: all senders share the bandwidth. As long as sum from all users is less than reservation, its OK (audio conference)
  Distinct: there is a reservation for each sender (video conference)
Shared
Distinct
Wildcard
Explicit
Wildcard Filter (WF)
Shared Explicit (SE)
Fixed Filter (FF)
N/A

## Slide 13: Reservation Merging
Reservations Merged at multicast split points
Merging only for reservations of the same style
Merged reservation is Least Upper Bound (LUB)
  LUB computation defined by service
  LUB is minimal reservation greater than those being merged
  LUB usually not either of merged reservations - no absolute order in multi-dimensional case
R1
R2
S1
S2
S1: 10 kb/s S2: 5 kb/s
S1: 8 kb/s S2: 10 kb/s
S1: 10 kb/s
S2: 10 kb/s

## Slide 14: Merging
Reservations not made at same time
New reservations goes up tree until it hits an existing reservation
Reservation stops if its less than current reservation
Else, reservation continues upwards
Existing reservation
New reservation

## Slide 15: Additional RSVP Features
PathTear message
  Destroys path state and all reservations
ResvTear message
  Destroys a single reservation
One Path With Advertising (OPWA)
  Actual reservation sent in PATH messages
  Uses Adspec object
Confirmations
  RESV can ask for unicast confirmation
  Confirmation occurs at first merge point
  Reservation can still fail upstream!
Non-RSVP clouds
  RSVP tunneled through non-RSVP clouds
  Allows incremental deployment

## Slide 16: Guaranteed Service Model
Guarantees
  Zero loss
  Delay less than some amount
  Bandwidth more than some amount
No guarantees on
  jitter
  minimum delay
PATH message
  contains leaky bucket of source
  as it traverses network, each router modifies some parameters
RESV message
  contains bandwidth reservation
  receiver can compute delay from reservation and parameters in PATH
Receiver chooses bandwidth based on desired delay

## Slide 17: Controlled Load Service
Guarantees are qualitative, not quantitative
  Service resembles service that would be seen in an unloaded network
  high rate of packets will be delivered
  delay seen by most packets not much more than minimum delay
Good for adaptive applications
Simpler implementation
Classifier and
Policer
Router

## Slide 18: Problems with Intserv and RSVP
Scalability
  Core routers need to handle individual reservations
  Number of reservations proportional to link speeds
  Soft state refresh imposes processing burden
  State storage of PATH and RESV state; PATH may not be used
  Cisco routers maxed out 2000 reservations
ISP Differentiation missing
Billing
  QoS useless without billing
  RSVP billing hard
    multi-lateral agreements needed
    metering needed
    handling route changes very complex
Multicast not used
“Prisoners Dilemma” Effect

## Slide 19: Goals of an Alternative
Allow a variety of services
  Intserv had only two
Unidirectional - send only
No per-flow or per-user state in the core
No per-flow signaling messages
Decouple application from QoS mechanism
Work with existing apps
  RSVP/Intserv require end system cooperation
Based on bilateral agreements only
Follow IP Scalability Model
  Fast and dumb in the core
  Slower and smarter in the periphery

## Slide 20: Solution: Differentiated Services (diffserv)
Bilateral customer/provider relationships
Service Level Agreements (SLA’s) established ahead of time
  10 Mb/s for web traffic, 5 Mb/s for all else
  5 Mb/s during the day, 2 Mb/s at night
Boundary routers classify packets from customers and mark them
Core treats packets solely on markings
Customer-Provider
Relationship
Customer-Provider
Relationship
DS Boundary
Router
Core Router
ISP 1
ISP2
ISP3

## Slide 21: Diffserv Operation
Customer establishes SLA ahead of time
  SLA also specifies Traffic Conditioning Agreement (TCA), describes what traffic should look like
Customer sends packets
DS Boundary router in SP network then:
  classifies packets
  meters packets
  drops packets
  shapes packets
Meter
Profile
Marker
Dropper
Shaper
Classifier
Conditioner
Packets
In
Packets
Out
DS Boundary Router

## Slide 22: DS Byte and Per Hop Behaviors
Markings are made in an 8 bit field in IP header
  Formerly the Type Of Service (TOS) byte - largely unused
  6 bits used - 64 values
At each router, DS byte value mapped to Per Hop Behavior (PHB)
  Specifies observable behavior packets of this type should receive
  Mapping same in each router
  Default mappings defined
CU = Currently Unused
DSCP = DS Code Point

## Slide 23: Per Hop Behaviors
Building Block for Services
  General purpose, configurable behavior
Small number standardized
Room left for experimental PHBs
Complex Services defined by complex mappings at boundaries to few PHBs
Core routers only know about PHBs
PHB Groups
  A set of PHBs who’s behavior is defined relative to each other
  Example: PHB A receives twice the bandwidth of PHB B
Two standardized PHBs
  Expedited Forwarding (EF) RFC 2598
  Assured Forwarding (AF) RFC 2597

## Slide 24: Expedited Forwarding PHB
Single PHB
Packets belonging to Behavior Aggregate (BA) receive a configurable amount of link bandwidth
Circuit Emulation Service
  Boundary router polices traffic
  Excess traffic discarded
  Traffic marked as EF
  Enough bandwidth provisioned for all packets in network
  Results in no queueing anywhere in network - low delay, no loss
Implementation Straightforward
  Weighted Fair Queueing (WFQ) with two queues
  Configure rate of WFQ to match service
  Priority Queueing also possible
    Requires careful policing at periphery

## Slide 25: Assured Forwarding PHB Group
Defines 12 PHBs
  Four classes
  Three drop preferences per class
For each class, bandwidth and buffering is configurable
Ordering of drop preferences within a class - lower preference means lower loss probability
Packets within a micro-flow never reordered
  Even if within different drop preferences
Implementation using Random Early Drop (RED)
  Each class has a single queue
  Packets dropped randomly when arriving
  Drop probability increases with increasing queue size
  Drop probability depends on drop preferences
  RED guarantees ordering within a flow

## Slide 26: Using diffserv for VoIP
Types of SLAs
  64 kb/s for all voice traffic
  Voice traffic receives half the delay of web traffic
User makes SIP calls, starts RTP stream
DS boundary router marks RTP packets with appropriate DS codepoint
Packet receives desired service
1
2
3
4
Ingress
router
Calling Party
Called Party
SIP Proxy
Calling Party’s
ISP Network
RTP

## Slide 27: Whats the Problem?
How to identify voice packets at the boundary router?
  RTP not a well-known port or protocol
  No way to identify RTP by itself
Solution I
  SIP Proxy extracts port/IP from SDP in 200 OK
  Configures DS boundary router dynamically
  Possibly configured through a third party policy server
1
2
3
4
5
6
Ingress
router
Calling Party
Called Party
SIP Proxy
Subscriber
Database
Calling Party’s
ISP Network
7

## Slide 28: Solution I drawbacks
Requires strong trust between Callers ISP and SIP Proxy
  Needed since proxy configures boundary router
  Not the case if proxy is provided by a dot com!!
  Separation of transport and signaling fundamental
Won’t work if media stream encrypted
Won’t work if SIP encrypted
Requires proxies to parse SDP
Lengthens call setup with database query
Complexity in SP network
Dependent on signaling protocol

## Slide 29: Solution II
End user sets the DS codepoint to indicate voice traffic
How does it work
  UA receives 200 OK
  Starts sending RTP
  Each RTP packet marked with a pre-agreed TOS value
  DS boundary polices and remarks
Benefits
  ISP and SIP provider can be totally separate
  Works with IPSEC and SIP encryption
  No additional call setup delays
  Independent of signaling protocol
Drawbacks
  End user application must know about diffserv
  Doesn’t work with older applications (I.e., Netmeeting)
  Requires configuration in UA to know DS codepoint
    DHCP possibility

## Slide 30: SIP and intserv
Simple usage
  SIP used to set up call
  After UAC gets 200 OK, sends PATH, and UAS sends RESV
  After UAS gets ACK, sends PATH, UAC sends RESV
  Total separation
Problem
  What if call succeeds and reservation fails??
INV
200 OK
ACK
PATH
RESV
PATH
RESV
RESVCONF
RESVCONF
Media
Caller
Callee

## Slide 31: Coupling of intserv and SIP
DCS Specification uses a two phase INVITE
New solution places preconditions in SDP with single INVITE
  Preconditions specify events that must happen before far side is alerted
  If conditions not met, call is rejected
  Conditions are for QoS and for security
INV
183 Progress
PRACK
PATH
RESV
PATH
RESV
RESVCONF
RESVCONF
Media
Caller
Callee
200 OK
ACK

## Slide 32: Conclusions
QoS an important part of the big picture for SIP
IETF has defined two mechanisms
  Differentiated Services (diffserv)
  Integrated Services (intserv)
  Current work on using both at the same time
Either usable for IP telephony
  Some issues to be resolved