## Slide 1: The Real Time Transport Protocol (RTP)
Jonathan Rosenberg
Chief Scientist

## Slide 2: Talk Overview
RTP Functions
The Big Picture
RTP Services
RTCP Services
Scaling RTCP
Aggregation

## Slide 3: RTP: What is it?
Real Time Transport Protocol
RFC 1889
  product of avt working group
  1996 proposed standard
  2000 draft standard (new rfc)
What does it do
  e2e transport of real time media
  optimized for multicast (Mbone)
  provides sequencing, timing, framing, loss detection
  provides feedback on reception quality
What does it do (cont)
  provides information on group members
  provides data to correlate audio and video and other media
Features
  Scales to huge multicast groups (millions)
  Works with any codec
    need payload format for each codec
  Flexible

## Slide 4: RTP: What isn’t it?
Doesn’t guarantee quality of service
  doesn’t reserve network resources
  doesn’t guarantee no loss or bounded delay
  can work with QoS protocols (RSVP)
Doesn’t provide signaling
  other protocols must be used to set up RTP (like SIP or H.323)
Not a specific protocol type
  Does not run directly ontop of IP
  Runs ontop of UDP
  No fixed port number

## Slide 5: RTP Stack
IP
UDP
RTP
RTCP

## Slide 6: Big Picture: RTP, SDP and SIP
End
User
End
User
Proxy
Proxy
IP Network
SIP w/ SDP
C=IN IP4 123.1.2.3
m=audio RTP/AVP 1122 0 1
m=video RTP/AVP 1130 98
a=rtpmap:98 h263
RTP

## Slide 7: RTP Components: Data + Control
Data aka RTP
  very confusing
Always on an even UDP port
Provides
  sequencing
  timing
  framing
  content labeling
  User idenfitication
Control = Real Time Control Protocol (RTCP)
Same address as data, but one higher port
Provides
  reception quality
  sender statistics
  participant information (multicast - Mbone)
  synchronization information

## Slide 8: Real Time Data Transport
Originator breaks stream into packets (segmentation)
  application layer framing (ALF)!!!
Packets sent; network may lose, delay, reorder packets
Must, at receiver:
  reorder
  recover
  resegment
  rescynchronize
  clock synchronization!
RTP Source
RTP Sink
RTP
Packets

## Slide 9: Transport System
Source
  Digitize Audio from mike
  Silence Suppression
  Echo cancellation
  Compress Audio
    G.711: 64 kbps
    G.729: 8 kbps
    G.723.1: 5.3/6.3 kbps
  Packetize Audio in RTP
  Send
Sink
  Receive packets
  Un-packetize
  decompress
  comfort noise generation
  reorder
  recover loss
  jitter buffer
  A/D conversion to speakers

## Slide 10: Jitter Buffer
Packets delayed differently
Must play them out periodically
Packets may arrive after designated playout time -> loss
Insert extra delay to compensate
May need to adapt this amount
time
pkts

## Slide 11: RTP Packet Header
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|V=2|P|X| CC |M| PT | sequence number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| timestamp |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| synchronization source (SSRC) identifier |
+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+=+
| contributing source (CSRC) identifiers |
| .... |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 12: RTP Header Fields
Version: 2
P: indicates padding (for encryption)
X: extension bit
CSRC count: for mixers (later)
M: Marker Bit: indicates framing
  audio codecs: first packet in talkspurt
  video: last packet in frame
Payload Type: indicates encoding
  in RTP packet allows changes per-packet
  Useful for:
    adaptation
    DTMF codec
    silence codecs
SN: defines ordering of packets
Timestamp: when packet was generated
SSRC: identifier
CSRC: list of mixed users

## Slide 13: RTP Timestamp
Tick units are dependent on codec
  For speech: 125 microseconds (standard 8 khz sampling rate)
  For video: 90 KhZ
  For audio: 44.1 KhZ (CD rate)
Gaps in TS, but not in SN mean silence
Initial value random for security
Video
  Timestamp represents time at beginning of frame
  Many packets may have same timestamp
Speech
  Time per packet may vary
  Depends on packetization: 20-100ms typical

## Slide 14: Mixers and Translators
Mixer = Bridge
  combines audio from many users into one stream
  CSRC list indicates users being mixed
Translator
  Converts from one format to another
  For low speed access links
MIXER
TRANSLATOR

## Slide 15: RTCP: Real Time Control Protocol
Sent by all participants
  both senders and receivers (think multicast)
Same address as data, different port (one higher)
Several RTCP Packet Types
  Sender Report (SR): from senders
  Receiver Report (RR): by receivers. Indicates reception quality
  Source Descriptor (SDES): describes participant
  BYE: sent when leaving
Sender Report
  SSRC of sender
  number of bytes sent
  number of packets sent
  wall time + RTP timestamp (for correlation)
  receiver report data
SDES
  CNAME of participant (unique)
  SSRC of participant
  name, address, email

## Slide 16: Real Time Control Protocol
Receiver Reports
  Block for each sender
  Per sender data contains
    SSRC of sender
    fraction lost from sender
    jitter seen fromsender
    highest SN received
    cumulative packets lost
    DLSR: delay since last SR
    LSR: time of last sender report
BYE packets
  reason for leaving
  for mixers, SSRC of those users leaving

## Slide 17: Compound RTCP Packets
Actual UDP packet contains many RTCP packets
Always starts with SR or RR
Always contains SDES
May contain BYE
UDP Hdr
SR Header
SR Data
SSRC1
RR Data
SSRC2
RR Data
SDES Header
Name
Email

## Slide 18: RTCP Announcement Interval
RTP used in large multicast groups (possibly thousands)
Everyone sends RTCP, even receivers
When to send RTCP?
Possibilities:
  Every T seconds: RTCP bandwidth linear with group size. Bad!
  Never: nahhh
  With N participants, every N*C seconds
Current RTCP Algorithm
  Estimate group size L
    listen for other RTCP packets
    Build up table of SSRC/CNAME
  Compute interval LC
    C depends on desired RTCP bandwidth and average RTCP packet size
  Randomize by 1/2 to 3/2
  Send packet, do it again

## Slide 19: Algorithm Subtleties
Algorithm slightly different for senders
  For senders, L is actually number of other senders
  Gives much more bandwidth to data senders
Participants must measure avg. RTCP size on the fly to compute C
RTCP defines a minimum interval of 5 seconds
First packet has minimum interval of 2.5 seconds
  speed up knowing who you’re talking to
Reconsideration Algorithm
  group sizes can be very dynamic

## Slide 20: Reconsideration Algorithm
Problem:
  Many users join group at same time
  Each thinks group size is 1
  Each sends packet right away!
Solution: Reconsideration
  Don’t send packet! Check if group size has increased. If so, reschedule packet
  That’s conditional reconsideration
Unconditional reconsideration
  Always reschedule packet
  If group size hasn’t change, random number redrawn
  Turns out this works much better… long story.
BYE Reconsideration
  Stop everyone from sending BYE if they all leave group at same time
Reverse Reconsideration
  If people leave, allow users to send packets more frequently right away

## Slide 21: Payload Formats
Each codec needs a way to be encapsulated in RTP
RFC1890 defines mechanisms for many common codecs
  G.711, G.729, G.723.1, G.722, etc.
  Some simple video
More complex codecs have their own payload format documents
  MPEG
  H.263 and H.261
Payload format defines
  How to break frame into packets
  extra fields needed below main RTP header
  How to recover missing packets (sort of)

## Slide 22: Special Payload Formats
Redundant Encodings
  Each packet contains two versions of voice
    Current frame
    Low bit rate encoding of previous frame
  When packet is lost, wait for next one!
  Introduces delay
  Needs many codecs at source
FEC Payload Format (RFC2733, issuing tomorrow)
  Use parity codes (XOR) to protect packets
  Take N packets, XOR them, get FEC packet
  Send FEC packet
  Can recover if any one of N packets is lost

## Slide 23: Special Formats
Aggregation
  Mix many users together in a single packet
  Useful for gateway to gateway communications
  Can also reduce overheads
Compressed RTP
  For dialup links
  Don’t send header, just send index
  Far side uses index to retrieve header, and then increments certain fields